## Slide 1: GPU PERFORMANCE ANALYSIS
Bob Crovella, 5/13/2020

## Slide 2: AGENDA
Analysis Driven Optimization
Understanding Performance Limiters
Metrics Review
Memory Bound Analysis
Compute Bound Analysis
Future Sessions
Further Study
Homework

## Slide 3: REVIEW: TOP-LEVEL PERFORMANCE CODING OBJECTIVES
3
Make efficient use of the memory subsystem
Efficient use of global memory (coalesced access)
Intelligent use of the memory hierarchy
shared, constant, texture, caches, etc.
Expose enough parallelism (work) to saturate the machine and hide latency
Threads/blocks
Occupancy Work per thread
Execution efficiency

## Slide 4: ANALYSIS DRIVEN OPTIMIZATION
4
Profile
Determine Limiter
Study, Reflect, Learn, Inspect
Optimize
Or determine
bottleneck

## Slide 5: ANALYSIS DRIVEN OPTIMIZATION
Memory Bound?
Compute
Bound?
Optimize
Perform Memory Limiter Analysis
Perform Compute
Limiter Analysis
Perform Latency Analysis
Yes
Yes
No
No

## Slide 6: TOP-LEVEL PERFORMANCE BEHAVIOR - LIMITERS
Memory Bound – A code is memory bound, when the measured memory system performance is at or close to the expected maximum. (saturate memory bus)
Compute Bound – A code is compute bound when the compute instruction throughput is at or close to the expected maximum.
Latency Bound – One of the indicators for a latency bound code is when neither of the above are true (both compute and memory performance are low).
(Analysis-driven) Optimization uses the above determination to direct code refactoring efforts in the first stage.
Limiting behavior of a code may change over the duration of its execution cycle.
It’s desirable to analyze small sections of code e.g. one kernel at a time

## Slide 7: METRICS FOR DETERMINING COMPUTE VS. MEMORY BOUND https://docs.nvidia.com/nsight-compute/NsightComputeCli/index.html#nvprof-metric-comparison
Latency metrics:
“sm efficiency”: smsp cycles_active.avg.pct_of_peak_sustained_elapsed
Memory metrics:
“dram utilization”: dram throughput.avg.pct_of_peak_sustained_elapsed “L2 utilization”: lts t_sectors.avg.pct_of_peak_sustained_elapsed “shared utilization”:
l1tex data_pipe_lsu_wavefronts_mem_shared.avg.pct_of_peak_sustained_elapsed
Compute metrics:
“DP Utilization”: smsp inst_executed_pipe_fp64.avg.pct_of_peak_sustained_active “SP Utilization”: smsp pipe_fma_cycles_active.avg.pct_of_peak_sustained_active “HP Utilization”: smsp inst_executed_pipe_fp16.avg.pct_of_peak_sustained_active
“TC Utilization”: sm pipe_tensor_op_hmma_cycles_active.avg.pct_of_peak_sustained_active
“Integer Utilization”:
smsp sass_thread_inst_executed_op_integer_pred_on.avg.pct_of_peak_sustained_active

## Slide 8: MEMORY BOUND
A code can be memory bound when either it is limited by memory bandwidth or latency.
For a memory bandwidth bound code, we will seek to optimize usage of the various memory subsystems, taking advantage of the memory hierarchy where possible.
Optimize use of global memory
Under data reuse scenarios, make (efficient) use of higher levels of the memory hierarchy, and optimize these usages (L2 cache, shared memory).
Take advantage of cache “diversification” using special GPU caches – constant cache, read-only cache, texture cache/memory, surface memory.
For a code that is memory bandwidth bound, we can compute the actual throughput vs. peak theoretical

## Slide 9: COMPUTE BOUND
A code is compute bound when the performance of a particular type of compute instruction/operation is at or near the limit of the functional unit servicing that type
Optimization strategy involves optimizing the use of that functional unit type, as well as (possibly) seeking to shift the compute load to other types
For a code that is dominated by a particular type (e.g. single precision floating point multiply/add) we can compare the actual throughput vs. peak theoretical.

## Slide 10: LATENCY BOUND
A code is latency bound when the GPU cannot keep busy (low occupancy) with the available/exposed parallel work.
The general strategy for a latency bound code will be to expose more parallel work
  Make sure that you are launching a large number of threads
  Increase the work per thread (e.g. via a loop over input elements)
  Use “vector load” to allow a single thread to process multiple input elements
  Strive for maximum occupancy

## Slide 11: PERFORMANCE LIMITER CATEGORIES
Memory Utilization vs Compute Utilization Four possible combinations:
Comp Mem
Compute Bound
Comp Mem
Bandwidth Bound
Comp Mem
Latency Bound
Comp Mem
Compute and Bandwidth Bound
11

## Slide 12: WHAT IS OCCUPANCY?
A measure of the actual thread load in an SM (SIMD Processor), vs. peak theoretical/peak achievable
CUDA includes an occupancy calculator spreadsheet https://docs.nvidia.com/cuda/cuda-occupancy-calculator/index.html
Higher occupancy is sometimes a path to higher performance
Achievable occupancy is affected by limiters to occupancy
Primary limiters:
Registers per thread (can be reported by the profiler, or can get at compile time)
Threads per threadblock
Shared memory usage

## Slide 13: FURTHER STUDY
Analysis Driven optimization:
http://on-demand.gputechconf.com/gtc/2012/presentations/S0514-GTC2012-GPU-Performance-Analysis.pdf
http://www.nvidia.com/content/GTC-2010/pdfs/2012_GTC2010.pdf
Google “gtc cuda optimization”
New tools blogs:
https://developer.nvidia.com/blog/migrating-nvidia-nsight-tools-nvvp-nvprof/
https://developer.nvidia.com/blog/transitioning-nsight-systems-nvidia-visual-profiler-nvprof/
https://developer.nvidia.com/blog/using-nsight-compute-to-inspect-your-kernels/